## Slide 1: Land Use Policy in Massachusetts Solar Incentive Programs Kaitlin Kelly Renewable Energy Program Coordinator
COMMONWEALTH OF MASSACHUSETTS
Charles D. Baker, Governor
Karyn E. Polito, Lt. Governor
Matthew A. Beaton, Secretary
Judith Judson, Commissioner
Rhode Island College, Providence, RI
November 15, 2017

## Slide 2: Evolution of Land Use Policy in MA Solar
Solar Carve-out I Program (SREC I) 653MW
All projects equally eligible
Solar Carve-out II Program (SREC II) 1616 MW
Market Sector, SREC Factors, and Managed Growth
  Higher incentive granted to prioritized sites
  Large, ground mounted, virtually net-metered projects in capped Managed Growth category (total 126MW)
  Growth of CSS/ Low Income Housing mitigated limiting impact of Managed Growth
Solar Massachusetts Renewable Target Program (SMART) 1600MW Goal
Executive Office of Energy and Environmental Affairs directed DOER to focus on land use in development of new program
Established Land Use Categories with associated incentive subtractors
  Category 1 (Ag/ Non-ag); Category 2; Category 3; Prohibited
Incentive adders for priority sites
Implementing land use performance standards

## Slide 3: SMART Land Use Policy
Incentive
“Location Based” adders to incentives
  Landfill and Brownfield
  Rooftop
  Solar Canopy
  Agricultural
  Floating Solar
Location based adders can be combined with an offtaker based adder, and a storage adder
Working with sister agencies in approving projects on unique locations
  Brownfield- MA Department of Environmental Protection
  Agricultural- MA Department of Agricultural Resources
  Floating Solar- MA Department of Environmental Protection/ MA Department of Fish and Wildlife
Disincentive
Greenfield Subtractor for certain categories of land use

## Slide 4: Adder Values
Energy Storage Adder | 
Type | Adder Value ($/kWh)
Storage + PV | Variable
Location Based Adders | 
Type | Adder Value ($/kWh)
Agricultural | $0.06
Building Mounted | $0.02
Brownfield | $0.03
Floating Solar | $0.03
Landfill | $0.04
Solar Canopy | $0.06
Off-taker Based Adders | 
Type | Adder Value ($/kWh)
Community Shared Solar (CSS) | $0.05
Low Income Property Owner | $0.03
Low Income CSS | $0.06
Public Entity | $0.02
Solar Tracking Adder | 
Type | Adder Value ($/kWh)
Solar Tracking | $0.01

## Slide 5: Encouraging Unique Design
Agricultural Generation Unit
Dual Use PV installations on working farm land, so that it will not interfere with continued land use
Raised structures spaced to allow crop growth, grazing animals, etc.
Required to provide annual reports on agricultural productivity
DOER developing further guidance with MDAR
Approval comes from DOER/ MDAR
Floating Solar
Installed on bodies of water used for agricultural or industrial activities (i.e. water treatment facilites)
Prohibited on natural waterbodies and wetland resource areas
Approval comes from DOER/ MassDEP

## Slide 6: Land Use Categories
All projects are categorized according to land use
Category 1- No Greenfield Subtractor
  Category 1 Agricultural (facilities located on Land in Agricultural Use or Prime Agricultural Farmland)
    Agricultural Solar Tariff Generation Units
    Building Mounted Solar Tariff Generation Units
    Solar Tariff Generation Units sized to meet no greater than 200% of annual operational load of an agricultural facility
  Category 1 Non-Agricultural
    Ground mounted <=500 kW
    Ground mounted >500 kW and <=5,000 kW that are (1) on land that has been previously developed or (2) on land in a solar overlay district or zoned for solar or power generation
    Building Mounted, Brownfield, Landfill, Canopy, and Floating Solar Generation Units
Category 2- Half Greenfield Subtractor
  Zoned Commercial/ Industrial and not previously developed
Category 3- Full Greenfield Subtractor
  All other project types
Ineligible Land Use
  Article 97 Land (unless it meets Category 1 criteria)
  Wetland Resource Areas
  Historical register sites (except as authorized by regulatory bodies)
Previously Developed is defined as having pre-existing paving, construction, or altered landscapes excluding alterations resulting from ag use, forestry, or use as a preserved natural area
Project Type | Category 3 | Category 2 | Category 1 | Rooftop | Brownfields | Landfill | Canopy
Compensation Rate ($/kWh) | X - $0.001/acre | X - $0.0005/acre | X | X + $0.02 | X + $0.03 | X + $0.04 | X + $0.06
Base Rate
Adders
Subtractors

## Slide 7: Land Use Performance Standards
All ground mounted facilities must comply with the following performance standards:
  No removal of all field soils
  existing leveled field areas left as is without disturbance
  where soils need to be leveled and smoothed, such as filling potholes or leveling, this shall be done with minimal overall impact with all displaced soils returned to the areas affected;
  ballasts, screw-type, or post driven pilings and other acceptable minimal soil impact methods that do not require footings or other permanent penetration of soils for mounting are required, unless the need for such can be demonstrated;
  any soil penetrations that may be required for providing system foundations necessary for additional structural loading or for providing system trenching necessary for electrical routing shall be done with minimal soils disturbance, with any displaced soils to be temporary and recovered and returned after penetration and trenching work is completed;
  no concrete or asphalt in the mounting area other than ballasts or other code required surfaces, such as transformer or electric gear pads;
  address existing soil and water resource concerns that may be impacted to ensure the installation does not disturb an existing soil and water conservation plan or to avoid creating a negative impact to soil and water conservation best management practices, such as stimulating erosion or water run-off conditions;
  limited use of geotextile fabrics; and
  maintain vegetative cover to prevent soil erosion

## Slide 8: Next Steps
SMART Regulations are fully in effect 225 CMR 20.00
DOER is currently developing further guidance on Land Use Categorization, to be released for comment in the coming weeks
Program will go into effect next year, likely around late Spring 2018
A 100MW RFP for ground mounted projects released November 13, 2017
  Open only to ground mounted projects
  Eligible projects subject to Greenfield Subtractor, cannot apply for adders
  Results announced January 11, 2018, setting all program prices

## Slide 9: Thank you
Visit our website:
https://www.mass.gov/solar-massachusetts-renewable-target-smart
Questions:
Kaitlin.Kelly@state.ma.us